## Slide 1: POWER SHARING METHOD FOR A DC MICROGRID
GROUP MEMBERS
2022/E/019
2022/E/020
2022/E/072
Notes: Good morning. In a DC microgrid, different sources operate together, and without proper coordination, the system can become unstable.
To solve this, we use a droop control strategy combined with a bidirectional DC-DC converter to ensure stable and balanced operation.
The main focus of our project is to maintain a stable DC bus voltage while allowing multiple energy sources, such as solar and battery storage, to share power properly.

## Slide 2: content
INTRODUCTION
PROBLEM
OBJECTIVE
METHODOLOGY
SYATEM ARCHITECHTURE
CONTROL AND POWER MANAGEMENT
SIMULATION SETUP
PLANNED WORK FOR FINAL STAGE
CONCLUSION

## Slide 3: INTRODUCTION
Renewable energy sources like solar power are increasing rapidly.
A DC microgrid is a local power system that connects renewable sources, battery storage, and DC loads to a common DC bus.
Many modern systems use DC loads such as EVs, LED lighting, and electronic devices.
Power sharing control that multiple energy sources in a DC microgrid supply the load together in a balanced manner while maintaining stable system operation.
Notes: Today, renewable energy like solar is widely used, but the problem is that it is not constant.
A DC microgrid is a localized power system where renewable sources, battery storage systems, and DC loads are connected to a common DC bus.
At the same time, many modern systems such as EVs and electronic devices operate on DC power.
But when we connect multiple sources like solar and battery to a common DC bus, we need proper power sharing to keep the system stable.”

## Slide 4: Problem
Solar voltage is variable due to changes in sunlight.
Load demand continuously changes depending on connected devices.
Battery voltage varies with its state of charge (SOC).
However, the DC bus voltage must remain constant.
Without proper control, unequal power sharing can cause voltage instability or source overloading.
Notes: The main issue in a DC microgrid is variability.
Solar power changes depending on sunlight. Load demand changes depending on how many devices are connected. Battery voltage changes based on its state of charge.
But even with all these changes, the DC bus voltage must remain constant.
If we don’t control it properly, one source may supply too much power, which can cause instability or overloading.

## Slide 5: OBJECTIVE
Design and simulate a DC microgrid system with a stable DC bus voltage by integrating a battery energy storage system using a bidirectional DC-DC converter, implementing droop control for balanced power sharing.
Notes: So our objective is simple.
We want to maintain a stable voltage DC bus while allowing multiple sources to share power automatically.
To do that, we use a bidirectional DC-DC converter for the battery, and we implement droop control along with a PI controller.
Finally, we validate everything using simulation

## Slide 6: METHODOLOGY
Design DC Microgrid Structure
Model Solar PV Source
Develop Bidirectional DC-DC Converter
Implement Droop Control (Vref = Vnom − kI)
Apply PI Controller for Voltage Regulation
Generate PWM for MOSFET Switching
Analyze Voltage, Current & Power Sharing
Simulate System in MATLAB/Simulink
Notes: In this project, we first designed the DC microgrid structure including the solar source, battery, DC bus, and load.
Then we modeled the battery and developed the bidirectional DC-DC converter in MATLAB/Simulink.
After that, we implemented droop control and a closed-loop PI controller for voltage regulation.
Finally, PWM switching was used to control power flow, and the complete system was simulated to analyze performance

## Slide 7: SYSTEM ARCHITECHTURE
Notes: In our system, solar and battery are connected to a common DC bus.
The battery is connected through a bidirectional converter.
This converter works in two modes:
When excess solar power is available, it charges the battery. When load demand is high, the battery discharges and supports the DC bus.
The DC bus voltage is maintained at constant voltage

## Slide 8: Control and Power Management
Bidirectional DC-DC Converter
Droop Control
Closed-Loop Voltage Control
PWM Switching Mechanism

## Slide 9: Bidirectional DC-DC Converter
Operates in Buck mode during battery charging.
Operates in Boost mode during battery discharging.
Controls energy flow between battery and DC bus.
Uses MOSFET switching controlled by PWM.
Ensures stable and efficient power transfer.

## Slide 10: Droop Control
Droop control adjusts the voltage reference based on output current.
When load increases, the reference voltage slightly decreases.
This enables automatic and balanced power sharing between sources.
No communication is required between converters.
The PI controller maintains the DC bus voltage constant.

## Slide 11: Droop Control
Vref = Vnom − kI
Vnom is the nominal DC bus voltage .
I is the output current supplied by the converter.
k is the droop gain that determines how much the voltage decreases with current.

## Slide 12: Closed Loop Voltage Control
PI controller processes error
Generates duty cycle
Stabilizes DC bus voltage
Error = Vref − Vdc

## Slide 13: PWM Switching Mechanism
PWM controls MOSFET switching in the converter.
A triangular carrier is compared with PI output to generate pulses.
Duty cycle determines energy transfer.
Switching frequency is around 10 kHz.
Regulates voltage and power flow.

## Slide 14: Simulation Setup
Here We using mange batterry system

## Slide 15: Simulation Setup

## Slide 16: Simulation Setup - Battery

## Slide 17: Simulation Setup - Battery

## Slide 18: Simulation Setup - Battery

## Slide 19: Simulation Setup - PV array

## Slide 20: Simulation Setup

## Slide 21: Simulation Setup

## Slide 22: Planned Work for Final STAGE
Implement a control strategy to manage the current sharing between different batteries based on their State of Charge (SOC).
Develop a charging and discharging mechanism so that each battery operates according to its SOC level to improve efficiency and battery life.

## Slide 23: CONCLUSION
A droop-controlled bidirectional converter maintains a stable voltage DC bus.
The combined droop control and PI-PWM mechanism enables automatic and balanced power sharing without requiring communication.
The proposed system improves voltage stability, reliability, and efficiency of the DC microgrid.

## Slide 24: THANK YOU !